## Slide 1: Basic Electronics
Generated by collegeAi
Generated by collegeAi

## Slide 2: Introduction
Basic electronics provides the foundation for understanding how circuits work. This lecture covers fundamental concepts like voltage, current, resistance, and key circuit laws, along with practical engineering frameworks.
Generated by collegeAi

## Slide 3: Section 1: Voltage, Current, and Resistance
**Voltage (V):** Electrical potential difference; the "push" that drives current (measured in Volts). V = Energy/Charge (V = W/q).
**Current (I):** Flow of electrical charge (measured in Amperes).
**Resistance (R):** Opposition to current flow (measured in Ohms). R = L/(σA), where L is length, σ is conductivity, and A is cross-sectional area.
Generated by collegeAi

## Slide 4: Section 2: Ohm's Law and Resistor Networks
**Ohm's Law:** V = IR. Relates voltage, current, and resistance.
**Resistors in Series:** Same current, resistances add (Req = R1 + R2 + ...).
**Resistors in Parallel:** Same voltage, reciprocal resistances add (1/Req = 1/R1 + 1/R2 + ...).
Generated by collegeAi

## Slide 5: Section 3: Kirchhoff's Laws
**Kirchhoff's Current Law (KCL):** Current entering a node equals current leaving.
**Kirchhoff's Voltage Law (KVL):** Sum of voltage sources in a loop equals the sum of voltage drops.
Generated by collegeAi

## Slide 6: Example
A simple circuit consists of a 9V battery and a 1kΩ resistor. Using Ohm's Law (V=IR), the current flowing through the resistor is I = V/R = 9V / 1000Ω = 0.009A (9mA).
Generated by collegeAi

## Slide 7: Summary
Voltage, current, and resistance are fundamental concepts in electronics.
Ohm's Law (V=IR) defines the relationship between these quantities.
Kirchhoff's Laws enable analysis of complex circuits.
Generated by collegeAi